## Slide 1
Dynamic Violin Fingerboard
Team 93
Adrian Ignaci, Kamil Waz, Sophia Wilhelm

## Slide 2
Introduction
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 3
Objective: Learn to Play Violin
Challenges:
  Costly Lessons
  Lack of Feedback
Problem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 4
Main Unit:
  Upload Songs
  Guide User through Piece
  Check Accuracy
Fingerboard Attachment:
  LEDs
  Potentiometer
Solution
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 5
The project is similar to some available products (such as light-up keyboards), but is unique due to
User uploaded pieces
Analog functionality
Detachability
  Swappable neck/board possibilities
Uniqueness
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 6
Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 7
Special Considerations:
  Small clearance of violin strings
  Non-uniform note spacing
  Non-destructive (detachable)
  Curved fingerboard surface
  Excessive weight
    Assume device point mass
    Scroll end -> 2.646 N (0.6lbf)
    Under body
Hardware
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 8
Lives in both input and output systems:
Processes location information and maps it to display values
Pros:
  Very flexible/adaptable
  Lots of GPIO
  Wireless functionality
  Some members have used it
Cons:
  More difficult hardware design
  Requires additional hardware to make viable
ESP32-WROOM-32 Microcontroller
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 9
ESP32 with Associated Extra Hardware
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 10
Consists of:
  Membrane potentiometer touch sensors (they can float!)
    SpectraSymbol SP-L-0100-103-3-ST
  ESP32 (For the Web Server)
    Web Server replaced USB functionality
Input System
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 11
LCD Screen (16x2)
Individually Addressable LEDs (FZ2812-5050)
  Must be specially spaced to properly display target locations
Output System
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 12
String Placements (mm)
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
 | G string | D String | A String | E String
Low 1st | 18 | 18 | 18 | 0
1st Finger | 36 | 36 | 36 | 18
2nd Finger | 68 | 52 | 52 | 52
High 2nd | 83 | 68 | 68 | 68
3rd Finger | 83 | 83 | 83 | 83

## Slide 13
  ESP32 can hit peaks of 500mA when running a web server!
  Assume all LEDs and LCD have a separate current source
  We must isolate the 5V and 3.3V lines:
    Each has a voltage regulator rated for 800mA
    Shut off web server when not in use
    Powered by 5000mA battery pack
Power System
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 14
High-Level Function
The FSM on the left is a basic representation of the software structure and use order of the product.
Note how each state contains multiple unique behaviors as opposed to a single change.
IMAGE
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 15
Software Design
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 16
Verification
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 17
Requirements/Verification: Output Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Requirements | Verification
Microcontroller <--> LEDs latency self-consistent within a variation tolerance of 7ms +- 1ms | Use oscilloscope to measure time between subsequent data packets

## Slide 18: 0'd at first packet Average of ~10ms latency with a deviation of 1ms.
Latency Results
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING
Packet 1: 0 ms
Packet 2: 10.119 ms
Packet 3: 20.045 ms

## Slide 19
Requirements/Verification: Input Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Requirements | Verification
Web server can upload a file of up to 1 MB in size within 10 seconds | Use a network analysis tool to measure the delay between sending a file and receiving a response from the server

## Slide 20
Upload of: IPR Test Document (1 MB)
IMAGE
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Upload of: Musette (1KB)
Upload of: Blank 1098 Form (1.2 MB)

## Slide 21: Upload time grows: y=0.34e0.0341x
Upload Time Equation
ELECTRICAL & COMPUTER ENGINEERING
GRAINGER ENGINEERING

## Slide 22
Requirements/Verification: Input Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Requirements | Verification
Detect user finger placement within 2mm +/- 0.1mm | Mark correct positions with tape; measure deviation from tape when correct note detected

## Slide 23
Requirements/Verification: Power Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING
Requirements | Verification
Consistent 3.3V +/- 5% voltage, 250mA current to the ESP32 | Use multimeter to measure voltage drop ESP --> GND
Consistent 5V +/- 5% voltage, 500mA current to LEDs, LCD | Use multimeter to measure voltage drop LEDs, LCD --> GND

## Slide 24
(Individual test)
  Power bank output 6.4 volts (>5)
  3.3 voltage regulator output 4.2 (>3.3)
(Multi-system test)
  Power button pin, ground at ground of 3.3 voltage regulator
  Vin got 1.36, and Vout got 0
Challenges and Failures: Power Subsystem
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 25
Pwr/Gnd pads ripped off (WEAK)
LED spacing sideways (between strings) very tight
  Inner LEDs not getting sufficient power
  Possible bridging
Not enough capacitors; needed:
  specific value
  *surface mount*
  lot of them (~20)
Challenges and Failures: Flexible PCB
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 26
Conclusion
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 27
  More constructive feedback for the user on the LCD display
  Implementing optical recognition software to read sheet music
  Cleaner exterior (housing, detachable system)
  Slimmer flexible PCB (thinner LEDs)
  USB option
  Detachable sensor arrays and software support for more instruments!
Future Improvements
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING

## Slide 28
Thank You
Questions, Comments, Concerns?
GRAINGER ENGINEERING
ELECTRICAL & COMPUTER ENGINEERING